AX.25 Version 2
			  Multi-channel
			  TNC  FIRMWARE

			 (version 0.91)

	    Copyright 1985, Ronald E. Raikes (WA8DED)



     This firmware supports the full AX.25  link-layer  protocol,
version 2.0 as described in the ARRL specification dated  October
1984,  as  well  as   the   pre-existing   version   1.x.    This
implementation supports multiple  simultaneous  link  connections
with either version protocol.  This release  has  been  assembled
for a maximum of four connections, although any reasonable number
of connections is possible by changing one MAXLNK symbol  in  the
source equate file.

     The firmware  is  contained  in  two  2764  EPROMs,  and  is
intended to be installed in a TAPR TNC-1 (or equivalent, such  as
the AEA PKT-1 or Heath HD-4040) in sockets  U11  and  U12.   This
assumes that a 6264 RAM is already installed in socket  U7,  with
additional 6264 RAMs optionally installed in sockets U8, U9,  and
U10 in any combination  Additional RAM  is  highly  desirable  if
multi-channel  or  unattended  operation  is  anticipated.   When
installing the EPROMs, it will be necessary to start the tnc with
the PARAMETER SOURCE switch set to the PROM position.  This  will
cause default parameters to be written into NOVRAM memory but not
PERMed.  The RS-232 port will be initialized  to  300  baud  with
xon/xoff handshaking.  The tnc  source  call  sign  will  be  all
blanks, and should be set with the 'I' command, as  well  as  any
other default parameters that might need changing, before issuing
a 'PERM' command.  At this point, the PARAMETER SOURCE switch may
be set to NOVRAM for subsequent operation.  If the terminal  baud
rate has been changed, the new value will take effect following a
reset.

     Commands and information are sent to the tnc in the form  of
lines.  Lines may be up to 256  characters  long,  including  the
terminating CARRIAGE RETURN.  If the 256th character  entered  is
not a CARRIAGE RETURN, it will be discarded and a BELL  character
will be output to the terminal.  BACKSPACE and DELETE may be used
to remove single characters from the line.  The entire  line  may
be permanently backspaced out by entering a CONTROL-U or CONTROL-
X.  A CONTROL-R will temporarily backspace out any  partial  line
to allow incoming frames to be  displayed.   A  second  CONTROL-R
will then restore  the  line  to  allow  continuation  of  entry.
During the time a partial line is saved, only  another  CONTROL-R
will be  accepted  from  the  keyboard  (with  the  exception  of
xon/xoff, of course).  BELL characters are echoed to the terminal
when entered or  removed.   Lines  which  begin  with  an  ESCAPE
character (echoed as '* ') are interpreted  as  commands.   If  a












command is issued with no parameter, the current  value  of  that
commands parameter is displayed.  An embedded NULL character in a
command will cause the remainder  of  the  line  to  be  ignored.
Lines without a leading ESCAPE character are sent as information.

     The firmware provides the operator  with  five  virtual  tnc
channels, numbered 0 to 4.  The terminal is logically attached to
only one of these  channels  at  a  time,  selected  by  the  'S'
command.  Information sent on channel 0 is always  unproto.   The
unproto path may be set by issuing a 'C' command when  channel  0
is selected.  Channels 1 - 4 are also unproto  if  they  are  not
currently connected.  Outgoing connect requests may be issued  on
any unconnected channel, while incoming connect requests will use
the first available  channel  (provided  the  maximum  number  of
connections set  by  the  'Y'  command  will  not  be  exceeded).
Information received on a connected channel that is not currently
selected will remain queued there until that channel is  selected
(the 'L' command is useful in determining if there is information
waiting on other channels).  Information for transmission is sent
only to the currently selected channel.   When  a  connection  is
ended,  any  information  that  has  not  been	 transmitted   or
acknowledged will be discarded.  Received information will remain
queued,  however,  until  it  has  been  displayed.   If  a   new
digipeater  path  is  desired  while  a   connection   is   being
established or is in progress, it is not necessary to  disconnect
first.  Simply re-issuing the 'C' command will  re-establish  the
connection via the new path  without  any  loss  of  information.
Attempting to connect to  the  same  station  on  more  than  one
channel is not permitted.

     Which protocol version is used to initiate a  connection  is
controlled by the 'V' command, but the version  will  be  changed
automatically, if necessary, to conform to the version of the tnc
responding.  Version 2 protocol is more  effecient  in  terms  of
network  throughput  and   loading,   especially   under   severe
conditions.  Version 2 protocol is the default and should be used
whenever possible.  (NOTE:  The  existing  firmware  supplied  by
TAPR for the TNC-1 (v3.x) will NOT digipeat version  2  protocol.
This is expected to  remedied  in  v4.0.   All  other  tnc's  and
digipeaters encountered to date  digipeat  version  2  properly.)
When version 2 protocol is used, a  watch-dog  timer  is  started
whenever information  is  not  being  transmitted.   If  the  tnc
remains idle for two minutes, it  will  poll  the  other  tnc  to
determine if the link is still established.  If  no  response  is
received after the number of tries set by the  'N'  command,  the
tnc will attempt to re-establish the connection.  This  procedure
will also detect the case where someone connects and then  leaves
without disconnecting.  Changing the protocol  version  during  a
connection is not permitted.

     The 'F', 'N', 'O',  and  'V'  commands  maintain  individual
parameters for each channel.  The value stored in  channel  0  is
the value that is  saved  in  NOVRAM.	This  value  is  used  to
initialize channels 1 - 4 after a  reset,  and  to  re-initialize












channels 1 - 4 after a disconnect.  This allows the values to  be
changed independently on each channel,  prior  to  and  during  a
connection, and then automatically revert back  to  the  standard
values when the connection is ended.  A 'D' command issued  on  a
disconnected channel 1 - 4 will also re-initialize that channel.

     Frame monitoring is controlled  by  the  'M'  command.   The
command parameter determines the types of frames  monitored,  and
is a list of desired  frames  chosen  from  the  letters  in  the
following table:

     LTR       FRAME
     ---       -----
      N        None
      I        I frames
      U        UI frames
      S        Supervisory frames
      C        Monitor while connected
      R        Monitor received frames (addressed to)
      T        Monitor transmitted frames (addressed from)

An asterisk displayed after a call sign in  the  digipeater  list
indicates the frame was transmitted by that station.  The control
field displayed will be one of the following:

     NAME   DESCRIPTION
     ----   -----------
     RRa  - Receive Ready
     RNRa - Receive Not Ready
     REJa - Reject
     UI   - Unnumbered Information
     DM   - Disconnected Mode
     SABM - Connect Request
     DISC - Disconnect Request
     UA   - Unnumbered Acknowledge
     FRMR - Frame Reject
     Iab  - Information
     ?ccH - Unknown

     a  = Next expected frame number (0 - 7)
     b  = Frame number of this frame (0 - 7)
     cc = Hexadecimal value

If the control field has the  poll/final  bit  set,  one  of  the
following characters will also be displayed:

     ! = poll/final bit (version 1)
     + = poll  bit (version 2)
     - = final bit (version 2)

The protocol identifier field is displayed in hexadecimal,  which
is currently  always  an  F0,  signifying  that  no  layer  3  is
implemented.













     An unattended mode, controlled by the 'U' command,  provides
for sending user supplied text to a connecting station, and  then
allows that station to leave a  brief  message.   This  mode  can
operate on all channels simultaneously, but in no way limits  the
operators ability to interact with one of the connected  channels
or  his  ability  to  make  outgoing  connect	requests.    When
unattended mode is enabled, link status messages  are  queued  to
the associated channel and not output to the terminal unless that
channel  is  currently  selected.   Link  status  messages   will
therefore  be  displayed  in   chronological   order   with   the
information from that channel.  In addition, text supplied by the
user with the 'U' command  will  be  sent  to  any  station  that
connects.  If channel 0  is  left  selected,  stations  may  then
connect and leave messages on channels 1 - 4 (limited by the  'Y'
parameter, of course).  The 'L' command may be used to  determine
if messages have been left on any channel.  Selecting  a  channel
containing messages will cause all link  status  and  information
from that channel to be displayed.  If  xon/xoff  handshaking  is
enabled, CONTROL-S and CONTROL-Q may  be  used  to  regulate  the
output to  the  terminal  to  allow  comfortable  reading.   Also
provided,  but  intended  to  be  used  very  sparingly,  is   an
unattended QST facility.  In this mode, user supplied text may be
automatically transmitted unproto to the path set on  channel  0,
at periodic intervals spaced  1  -  65,535  minutes  apart.   The
interval and text must be entered each time QST mode is  enabled.
Use of unattended QST messages is generally degrading to  network
performance and is considered by many to  be  an  annoyance,  and
should only be used when absolutely necessary.

     The tnc parallel port supplies link status  information  for
channel 1 on lines PA0, PA1, and PA2 for  use  with  an  external
status indicator.  The following link states are possible:

		    1 = Disconnected
		    2 = Link Setup
		    3 = Frame Reject
		    4 = Disconnect Request
		    5 = Information Transfer

     The firmware source is written in  6809  assembly  language.
Emphasis was  placed  on  using  a  state  table  driven  design,
utilizing the state tables provided in  the  ARRL  specification.
The source was assembled using a 6809 cross assembler  from  2500
AD Software running on a Z-80/8086  TurboDOS  development  system
(CP/M & MS-DOS compatable).





















NOTE:	A  very  small  number  of  Western  Digital  1933   HDLC
Controller ICs manufactured in 1981 and 1982 have been  found  to
be defective.  The symptoms are erratic and unreliable  operation
of the tnc, due to the hdlc controller  occasionally  failing  to
interrupt  upon  successful  completion  of  frame  transmission.
These defective parts can be identified by  inspecting  the  mask
number on the underneath side of  the  IC.   The  defective  mask
number begins with the letters 'BA', and should be replaced.  The
current replacement part is called 1935 and requires no changes.

























































			 COMMAND SUMMARY
			 ===============



COMMAND        PARAMETER	       DESCRIPTION
-------        ---------	       -----------

  A (1)		   0		 Auto linefeed disabled
		   1		 Auto linefeed enabled

  B (6)		  1-15		 Terminal baud rate

* C	   Cs1 [Cs2 ... Cs9]	 Connect path (0=unproto path)

* D				 Disconnect

  E (1)		   0		 Echo input disabled
		   1		 Echo input enabled

* F (4)		  1-15		 Frame acknowledge (seconds)

  G		  [0]		 Get information (host mode)
		  [1]		 Get link status (host mode)

  H (1200)	 50-9600	 HDLC baud rate

  I		   Cs		 Tnc source call sign

  JHOST (0)	   0		 Terminal mode enabled
		   1		 Host mode enabled

  K		  1-2		 Calibrate

  L		 [0-4]		 Display channel status

  M (3)		  0-255		 Monitor mode

* N (10)	  0-255		 Number of tries (0=forever)

* O (4)		  1-7		 Number of outstanding I frames

  PERM				 Save parameters to NOVRAM

  QRES				 Re-start firmware

  R (1)		   0		 Repeater disabled
		   1		 Repeater enabled

  S (1)		  0-4		 Select channel (0=unproto)

  T (4)		  1-16		 Transmitter delay (40ms)

  U (0)   0	 [text]		 Unattended mode disabled












	  1	 [text]		 Unattended mode enabled
	  2    interval  text	 QST mode enabled

* V (2)		   1		 Version 1 protocol initiated
		   2		 Version 2 protocol initiated

  W (2)		  0-15		 Repeater wait (40ms)

  X (1)		   0		 Transmitter PTT disabled
		   1		 Transmitter PTT enabled

  Y (1)		  0-4		 Maximum connections

  Z (3)		   0		 Flow disabled, xon/off disabled
		   1		 Flow enabled, xon/off disabled
		   2		 Flow disabled, xon/off enabled
		   3		 Flow enabled, xon/off enabled

  @	  B			 Display number of free buffers
	  C (0)    0		 Fast clock disabled
		   1		 Fast clock enabled
	  P (F0)  0-FF		 Protocol id (hex)
	  S			 Display current link state


   Default values are shown in parenthesis
*  These commands are applicable to each connection channel
     (Values set on channel 0 are used after a reset and
      disconnect to initialize each connection channel)





































		       COMMAND DESCRIPTION
		       ===================



     The 'A' command is used to enable or disable  the  automatic
insertion of LINEFEED characters after CARRIAGE RETURN characters
to the terminal.  This parameter is stored in NOVRAM.

     The 'B' command is used to set the terminal baud rate, using
one of the following parameters:

     Parameter	   Baud rate
     ---------	   ---------
	 1	      50
	 2	      75
	 3	      110
	 4	      135
	 5	      150
	 6	      300
	 7	      600
	 8	      1200
	 9	      1800
	10	      2400
	11	      3600
	12	      4800
	13	      7200
	14	      9600
	15	      19200

After setting the baud rate with the 'B' command, the value  must
be PERMed, and will then take effect  following  a  reset.   Baud
rates above  4800  may  not  be  reliable  with  sustained  input
(commands or information) from a host computer due  to  the  slow
cpu clock rate and non-vectored interrupt architecture.

     The 'C' command is used to initiate a link connection.  Note
that NO 'v' or 'via' is used between the  destination  call  sign
and the digipeater call signs.  A 'C' command may be issued on  a
channel already in use to change the digipeater call  signs,  but
not the destination call sign.  A 'C' command issued when channel
0 is selected sets the unproto path.  Attempting  to  connect  to
the same station on more than one channel is not permitted.

     The 'D' command is used to initiate a link disconnection.  A
'D' command issued during the establishment or  dis-establishment
of a link will cause an  immediate  return  to  the  disconnected
state.  A 'D' command issued on a disconnected channel  will  re-
initialize the connection  dependent  parameters  to  the  values
stored in channel 0.

     The 'E' command is used to enable or disable the echoing  of
input (commands and information) to the terminal.  This parameter
is stored in NOVRAM.













     The 'F' command is used to  set  the  frame  acknowledgement
interval.  This interval is used to compute the timeout  interval
before a packet is retransmitted, using the formula:

     time (seconds) = frame ack * (2 * number of digipeaters + 1)

A separate frame acknowlegement interval value is maintained  for
each connection channel.  The value stored in channel 0  is  used
to  initialize  each  connection  channel  after   a   reset   or
disconnection, and is the value that is stored in NOVRAM.

     The 'G' command is used to interrogate virtual tnc  channels
when host mode is enabled.  If no  parameter  is  specified,  the
next chronological item (information  or  link  status)  will  be
returned, provided there is one.   This  command  is  invalid  in
terminal  mode.   A  later  section  is  devoted  to  host   mode
operation.

     The 'H' command is used to set the  HDLC  baud  rate.   Non-
standard values are rounded down to the next possible baud  rate.
In this case, use an 'H' command with no paramter to display  the
value actually set.  This parameter is stored  in  NOVRAM.   HDLC
rates up to 9600 baud are supported if the  fast  clock  mode  is
enabled.

     The 'I' command is used to set the  tnc  source  call  sign.
The initial value is all blanks.  After the source call sign  has
been entered, the 'PERM' command should be used to  save  it  for
use during subsequent operation.

     The 'JHOST' command is used to select between  terminal  and
host modes.  A later section is devoted to host mode operation.

     The 'K' command is used to calibrate  the  tnc  modem.   The
following parameters set the calibration modes listed:

     Parameter	       Calibration
     ---------	       -----------
	 1	    FREQUENCY COUNTER
	 2	    TONE LEVEL & NULL

The frequency counter mode will display the measured  frequencies
on the terminal.  When each mode is  selected,  jumpers  settings
are displayed as well as the appropriate ajustment  points.   The
values shown in parenthesis are the normal targets for 1200  baud
operation.

     The 'L' command is used to display the link status of one or
all channels.	Information  displayed  includes  the  connection
path, number of receive frames not yet displayed, number of  send
frames not yet transmitted, number of transmitted frames not  yet
acknowledged, and the  current  retry  count.	A  '+'  character
preceeding the channel number indicates  the  currently  selected












channel.  Operation of this command when host mode is enabled  is
somewhat different, and is described in a later section.

     The 'M' command is used to set the  frame  monitoring  mode.
The command parameter determines the types of  frames  monitored,
and is a list of desired frames chosen from the  letters  in  the
following table:

     LTR       FRAME
     ---       -----
      N        None
      I        I frames
      U        UI frames
      S        Supervisory frames
      C        Monitor while connected
      R        Monitor received frames (addressed to)
      T        Monitor transmitted frames (addressed from)

This parameter is stored in NOVRAM.

     The 'N' command is used to set the maximum number of times a
frame  will  be  transmitted  without  receiving  an  appropriate
acknowledgement, before a link failure is  assumed.   A  separate
maximum number of tries value is maintained for  each  connection
channel.  The value stored in channel 0  is  used  to  initialize
each connection channel after a reset or  disconnection,  and  is
the value that is stored in NOVRAM.

     The 'O' command  is  used  to  set  the  maximum  number  of
unacknowledged I frames that may be outstanding at any one  time.
A separate maximum number of unacknowledged  I  frames  value  is
maintained for each connection  channel.   The  value  stored  in
channel 0 is used to initialize each connection channel  after  a
reset or disconnection, and  is  the  value  that  is  stored  in
NOVRAM.

     The 'PERM' command is used to change  the  parameter  values
stored in NOVRAM to those that are currently set.

     The 'QRES' command is used to restart the firmware as  if  a
hardware reset had been issued.

     The 'R' command is used to enable or disable the digipeating
of frames.  This parameter is stored in NOVRAM.

     The 'S' command  is  used  to  select  the  current  channel
number.  This parameter is stored in NOVRAM.

     The 'T' command is used to set the transmitter  keyup  delay
interval.  The parameter is specified in 40ms  increments.   This
parameter is stored in NOVRAM.

     The 'U' command is used  to  enable  or  disable  unattended
modes.  If QST mode is not used, previously entered text will  be












retained if new text is not provided.  If QST mode  is  selected,
the interval and text must be  supplied.   The  QST  interval  is
specified in minutes from 1 - 65,535.

     The 'V' command is used to select whether  version  1  or  2
protocol will be used to initiate a link connection.  A  separate
protocol version value is maintained for each connection channel.
The value  stored  in  channel  0  is  used  to  initialize  each
connection channel after a reset or  disconnection,  and  is  the
value that is stored in  NOVRAM.   Interrogating  this  parameter
during a connection will reflect the protocol  version  currently
being used on that channel.  Changing the protocol version during
a connection is not permitted.

     The 'W' command is used to set the digipeater wait interval.
The parameter is specified in 40ms increments.  This parameter is
stored in NOVRAM.

     The 'Y' command  is  used  to  set  the  maximum  number  of
connections that may  established  by  incoming  requests.   This
command has no  effect  on  the  operators  ability  to  initiate
outgoing  connection  requests.   This  parameter  is  stored  in
NOVRAM.

     The 'Z' command is used to enable or  disable  flow  control
and xon/xoff handshaking to the terminal.   If  flow  control  is
enabled, output to the terminal will be inhibited while  entering
commands or information.  If flow control is disabled, output  to
the terminal will not be restricted.  Flow control  and  xon/xoff
handshaking should be disabled during periods in which the tnc is
operated without a terminal, to  avoid  suspending  output  which
will consume buffers.  If xon/xoff handshaking  is  enabled,  crt
scrolling may be stopped and started using CONTROL-S and CONTROL-
Q characters.  Flow control  and  xon/xoff  handshaking  are  not
performed when host mode is enabled.  This parameter is stored in
NOVRAM.

     The '@'  command  is  a  software  maintenance  command.	A
parameter of 'B' will display the  number  of  free  buffers.	A
parameter of 'C0' will select timing parameters  for  the  slower
cpu  clock  rate.   A  parameter  of  'C1'  will  select   timing
parameters for the faster cpu clock rate.  The 'C'  parameter  is
stored in NOVRAM and must be PERMed if the change is to  stay  in
effect following a reset or power-up.  The 'P' parameter is  used
to set the protocol id byte for each channel and is supplied  and
displayed in hexadecimal.  A parameter of 'S'  will  display  the
current link state.



















		       HOST MODE OPERATION
		       ===================



     Host mode is intended to provide a user  interface  suitable
for operation under control of a host  processor.   Commands  and
information to the tnc, as well as status  and  information  from
the tnc, are clearly identified to allow orderly and  unambiguous
communication.  To alleviate any need for  hardware  or  software
handshaking,  the  tnc  will  not  send  to  the  host  processor
unsolicited,  and  all  exchanges  are  limited  to  256   bytes.
Information transfers are fully transparent.

     When host mode is enabled, the first byte sent to the tnc is
a channel number.  Information and commands are sent to  the  tnc
in similar formats, identified by the second byte.  If this  byte
is a binary 0, what follows is assumed  to  be  information.   If
this byte is a binary 1, then a command must follow.   The  third
byte sent is the length of the  actual  information  or  command,
decremented  by  1  (vacuous  information  or  commands  are  not
permitted).  The actual information or command bytes follow last.
Information sent to channel 0 or an unconnected  channel  1  -  4
will be sent unproto.  The tnc will respond with a channel number
followed by a binary code of 0, 1, or 2,  signalling  success  or
failure.  Codes of 1 or 2 will be followed by a  null  terminated
message.  Channels may be interrogated for  incoming  information
or link status by using the 'G' command.  The  tnc  will  respond
with a channel number first, followed by a binary code  of  0  if
nothing is available, or with 3 - 7, identifying the  bytes  that
follow.  Monitor headers and monitor information will  always  be
sent to  channel  0,  along  with  connect  request  link  status
messages.  All other link status messages will  be  sent  to  the
appropriate  channel,  along   with   that   channels	connected
information.  A code of 4 indicates the monitored frame does  not
contain  an  information  field.   A  code  of  5  indicates  the
monitored frame does contain an information field, and  the  next
'G' command on channel 0  will  return  that  information  field,
preceeded by a code of 6.

	 Host to Tnc
	 -----------

CHANNEL   CODE		 DESCRIPTION
-------   ----		 -----------
   ?	   0	    Information (preceeded by length-1)
   ?	   1	    Command	(preceeded by length-1)



















	 Tnc to Host
	 -----------

CHANNEL   CODE		 DESCRIPTION
-------   ----		 -----------
   ?	   0	    Success (nothing follows)
   ?	   1	    Success (message follows, null terminated)
   ?	   2	    Failure (message follows, null terminated)
   ?	   3	    Link Status (null terminated)
   ?	   4	    Monitor Header (null terminated)
   ?	   5	    Monitor Header (null terminated)
   ?	   6	    Monitor Information (preceeded by length-1)
   ?	   7	    Connect Information (preceeded by length-1)

Success messages
----------------

{channel status}
{parameter value}
CHANNEL NOT CONNECTED

Failure messages
----------------

INVALID COMMAND
TNC BUSY - LINE IGNORED
CHANNEL ALREADY CONNECTED
STATION ALREADY CONNECTED

Link Status messages
--------------------

BUSY fm {call} via {digipeaters}
CONNECTED to {call} via {digipeaters}
LINK RESET fm {call} via {digipeaters}
LINK RESET to {call} via {digipeaters}
FRAME REJECT fm {call} via {digipeaters}
FRAME REJECT to {call} via {digipeaters}
DISCONNECTED fm {call} via {digipeaters}
LINK FAILURE with {call} via {digipeaters}
CONNECT REQUEST fm {call} via {digipeaters}

Monitor Header format
---------------------

fm {call} to {call} via {digipeaters} ctl {name} pid {hex}




















Channel Status format
---------------------

a b c d e f

a = Number of link status messages not yet displayed
b = Number of receive frames not yet displayed
c = Number of send frames not yet transmitted
d = Number of transmitted frames not yet acknowledged
e = Number of tries on current operation
f = Link state

    Possible link states are:

     0 = Disconnected
     1 = Link Setup
     2 = Frame Reject
     3 = Disconnect Request
     4 = Information Transfer
     5 = Reject Frame Sent
     6 = Waiting Acknowledgement
     7 = Device Busy
     8 = Remote Device Busy
     9 = Both Devices Busy
    10 = Waiting Acknowledgement and Device Busy
    11 = Waiting Acknowledgement and Remote Busy
    12 = Waiting Acknowledgement and Both Devices Busy
    13 = Reject Frame Sent and Device Busy
    14 = Reject Frame Sent and Remote Busy
    15 = Reject Frame Sent and Both Devices Busy



NOTE 1:  Only items a and b are displayed for channel 0.

NOTE 2:  Only states 0 - 4 are possible if version 1 is in use.






























		       DEFAULT PARAMETERS
		       ==================



     In some instances, it  may  be  desirable  to  have  default
parameters which differ from the standard values.  To allow  easy
access, all default parameters have been placed at the  beginning
of the EPROM.  The following listing defines the layout  of  this
area:

     TYPE     VALUE	     DESCRIPTION
     ----     -----	     -----------
     BYTE      1BH	     COMMAND CHARACTER
     BYTE     '      ',60H   SOURCE CALL SIGN (SEE NOTE 1)
     WORD     000AH	     HDLC BAUD RATE DIVISOR (SEE NOTE 2)
     BYTE      06H	     TERMINAL BAUD RATE
     BYTE      01H	     MAXIMUM CONNECTIONS
     BYTE      03H	     MONITOR MODE (SEE NOTE 3)
     BYTE      01H	     REPEATER DISABLE/ENABLE
     BYTE      02H	     REPEATER WAIT (40ms)
     BYTE      04H	     TRANSMITTER DELAY (40ms)
     BYTE      03H	     FLOW CONTROL MODE
     BYTE      01H	     TRANSMITTER PTT DISABLE/ENABLE
     BYTE      01H	     CHANNEL NUMBER
     BYTE      01H	     AUTO LINEFEED DISABLE/ENABLE
     BYTE      01H	     ECHO COMMAND LINE DISABLE/ENABLE
     BYTE      01H	     VERSION 2 INITIATED DISABLE/ENABLE
     BYTE      04H	     MAXIMUM UNACKNOWLEDGED FRAMES
     BYTE      0AH	     MAXIMUM TRY COUNT
     BYTE      04H	     FRAME ACKNOWLEDGE INTERVAL
     BYTE      00H	     FAST CLOCK DISABLE/ENABLE
     BYTE      F0H	     PROTOCOL ID
     BYTE     'CQ    ',60H   UNPROTO CALL SIGN (SEE NOTE 1)


  DISABLE = 00H / ENABLE = 01H


NOTE 1:  The secondary station id must be shifted  left  one  bit
and or'ed with 60H.


NOTE 2:  The  HDLC  baud  rate  divisor  is  computed  using  the
formula:

SLOW CLOCK:	divisor = (14400 / buad rate) - 2

FAST CLOCK:	divisor = (28800 / buad rate) - 2

The HDLC baud rate divisor is stored most significant byte first.















NOTE 3:  The monitor mode is composed from the following bits:

     BIT       FRAME
     ---       -----
      0        I frames
      1        UI frames
      2        Supervisory frames
      4        Monitor while connected
      4        Monitor received frames (addressed to)
      5        Monitor transmitted frames (addressed from)